ORDER

№ A 615

Sofia, 24.10.2022

TECHNOTEST AD, Sofia

PRODUCT CERTIFICATION BODY, „ASSESSMENT" DIRECTION

Management and office address: 1528, Sofia, Iskar quarter, 10 Poruchik Nedelcho Bonchev Str.

To perform certification of products, according to the following scope:

| Scope type: flexible* |
| --- |
| № | PRODUCTS | CERTIFICATION SCHEME** | BASIC DOCUMENTS (STANDARD / REGULATORY DOCUMENT) |
| 1 | 2 | 3 | 4 |
|  | Safes | Scheme A Scheme B Scheme C | БДС EN 1143-1 БДС EN 15659 БДС EN 14450 TC*** |
|  | Treasury premises | Scheme A Scheme B Scheme D | БДС EN 1143-1 TC*** |
|  | Vault doors | Scheme A Scheme B Scheme C | БДС EN 1143-1 TC*** |
|  | Deposit systems | Scheme A Scheme B Scheme C | БДС EN 1143-2 (without additional testing and GAS classification – item 9.4 and item 10.4) TC*** |
|  | Doors, windows, shutters and grilles (blinds) | Scheme A Scheme B Scheme C | БДС EN 1627 БДС EN 1522 TC*** |
|  | Protective glasses. | Scheme A Scheme B Scheme C | БДС EN 356 БДС EN 1063 TC*** |

Remark: The introduction of a new version of the standards or standards that replace them is allowed. An up-to-date list of standards with their dated versions is provided by the CAB.

**Scheme A - Product certification, by testing samples taken by the customer, accompanied by an assessment of the technical documentation and the production process. PCB supervises the product / customer.

**Scheme B - Product type certification through testing and evaluation of samples, and technical documentation provided by the customer.

** Scheme C - Certification of a batch of product, by testing samples taken from the batch and comparing with the technical documentation of the product.

** Scheme D - Certification of a unique product on the basis of its technical documentation, certificates and/or protocols from testing of its elements and control during its production / construction. PCB supervises the product.

*** Technical specifications (including only requirements specified in the defined scope of certification and which do not contradict the accepted standards)