SCOPE 12 ЛК

SGS Bulgaria Ltd.

Calibration laboratory SGS Bulgaria

Management address:

1784 Sofia, Mladost District, 115G Tsarigradsko shose Blvd,

Megapark Business Center, Office C, floor 6

Laboratory address: 8008 Burgas, Transportna Str, Condosco Business Center, office 4

To perform calibrating of:

| Type of the the scope: fixed |
| --- |
| № | Measuring instrument | Measured value, unit of measure | Measurement Range | Calibration and measurement capability (CMC) | Calibration method |
| 1 | 2 | 3 | 4 | 5 | 6 |
| 1. | Tanks of different shapes | Volume, m3 | From 1 m3 to 75 m3 | 0,20 % | ISO 4269:2001 Volume method |
| 2. | Horizontal tanks | Volume, m3 | From 1 m3 to 300 m3 | 0,20 % | ISO 12917-1:2017 Tape method |
| 3. | Vertical, cylindrical tanks | Volume, m3 | From 1 m3 to 1 000 m3 | 0,20 % | БДС ISO 7507-2:2022 Optical-reference-line method or electro- optical distance ranging method |
|  |  |  | From 1 000 m3 to 10 000 m3 | 0,15 % |  |
|  |  |  | From 10 000 m3 to 50 000 m3 | 0,10 % |  |
|  |  | Volume, m3 | From 10 m3 to 50 000 m3 | 0,15 % | ВЛМК 1:2015 Electro-optical method |
|  |  | Volume, m3 | From 100 m3 to 50 000 m3 | 0,15 % | БДС ISO 7507-4:2016 Electro-optical method |

Note: Calibration is performed on-site at the customer’s premises.

Fixed scope references:

ВЛМК 1:2015 Method for calibration of vertical cylindrical tanks by geometric method through electro-optical measurement